Operation: Awesome
Matthew Branstetter
Vernon Jones
Yusuf Qedan
Tyler Tricker

---
Motivation
- To design a project that follows current standards and practices used in industry
- Develop team cohesion and work on communication skills

---
Objective
- To create a blinking Frisbee that adheres to the project requirements and specifications
- Have a working project and demonstrate at the completion of Fall term

---
Alternatives
- WHAMMO Frisbee Disc Twilight Blast - $19.99
  - 150 grams
  - 2 LEDs diffused through plastic
  - Runs off of 3 LR44 batteries
- Flashflight - $19.99
  - 185 grams
  - 1 super right LED diffused through plastic
  - Runs off of 2 CR2016

---
Requirements
- Have one or more inputs or sensors
- Have one or more outputs or transducers
- Have one or more processor modules
- Two layer PCB
- Have components that can be hand soldered or easily soldered in a crude reflow

---
Our Approach
- Our method was a top down approach to design
- Broke the project into interface module and LED module
- Developed modules independently
- Then combined the two on completion for the final design

---
Design: UML

---
Design: UML

---
Design: Software Algorithm

---
Light-up Frisbee Level 0 Block Diagram
Light-up Frisbee Level 0 Block Diagram
Light-up Frisbee
Power 5-7V
10 RGB LEDs
Module	Light Up Frisbee
Inputs	Power 6V from 2 lithium batteries
Outputs	10 RGB LED’s 40 pins common anode configuration
Functionality	Based on the measured angular velocity 10 RGB LEDs will light up different patterns and colors

---
Light-up Frisbee Level 1 Block Diagram
Light-up Frisbee Level 1 Block Diagram
Logic Power Supply
Power 5v-7V
3.3 V
Lighting Module
Row
Strobe
and
Reset
3.3 V
RGB
LED Outputs
Logic Module
Red Column
Blue Column
Green Column

---
Logic Power Supply: Level 0 Block Diagram
Logic Power Supply: Level 0 Block Diagram
Logic Power Supply
Power 5-7V
Power 3.3V
Module	Logic Power Supply
Inputs	Power 5-7V from 2 lithium batteries
Outputs	Power 3.3V
Functionality	Maintains a constant output voltage of 3.3V

---
Logic Power Supply: Level 1 Block Diagram
Logic Power Supply: Level 1 Block Diagram
Voltage Regulator
Power 3.3V
Power 5-7V
Diode
Cap
Cap
Decoupling

---
Logic Module: Level 0 Block Diagram
Logic Module: Level 0 Block Diagram
Logic Circuit
Row Strobe
Row Reset
Power 3.3V
Red Column
Blue Column
Green Column
Module	Logic Circuit
Inputs	Power 3.3V
Outputs	Row Strobe – Signal to the lighting circuit to activate the next LED.	Red Column – Turn Red on or off
	Row Reset - Signal to the lighting circuit to return to LED0.	Blue Column –Turn Blue on or off
		Green Column – Turn Green on or off
Functionality	Measures a rotational velocity and outputs lighting signals as a function of the rotational velocities value.

---
Logic Module: Level 1 Block Diagram
Logic Module: Level 1 Block Diagram
Gyroscope
Power 3.3V
ZOUT
Row Strobe
Row Reset
ATTINY461A
Red Column
Blue Column
Green Column

---
Lighting Module: Level 0 Block Diagram
Lighting Module: Level 0 Block
5-7 V
3.3 V
Lighting Module
Row
Strobe
and
Reset
RGB
LED Outputs
RGB
Strobe
Module	Logic Circuit
Inputs	Row Strobe – Signal to the lighting circuit to activate the next LED.	Red Column – PWM for red brightness
	Row Reset - Signal to the lighting circuit to return to LED0.	Blue Column – PWM for blue brightness
		Green Column – PWM for blue brightness
Output	10 RGB LED Outputs
Functionality	Takes lighting signals from the Logic Module and pulses LEDs according to the signal

---
Lighting Module: Level 1 Block Diagram
Lighting Module: Level 1 Block Diagram
5-7V
3.3 V
4017 Decade Decoder
Transistor Array
Row
Strobe
and
Reset
RGB LED
Anode
Outputs
Transistor Array
Current
Limiter
Red Column
Green Column
Blue Column
RGB
Strobe

---
Lighting Design Selection
Matrix Layout
Pin~Complexity = 2 cdot log_2{N}

---
Lighting Design Selection
Shift Register Layout
Pin~Complexity = K

---
Lighting Design Selection
Counter layout
Pin~Complexity = {N} over {5}

---
Design: Decisions Made
- Processor module – AVR suggested
  - AT mega
    - 256KB flash
    - 28-100 I/O pins
    - 20 MHz
  - AT tiny
    - 8KB flash
    - 6-32 I/O pins
    - 20 MHz
  Decision: AT tiny461A

---
Design: Decisions Made
- Gyro Sensor
  - Digital
    - Interface with Processor module
    - Expensive
  - Analog
    - AVR Analog/Digital converter
    - Cheaper
  Decision: STMicroelectronics LY3200ALH

---
Design: Decisions Made
- Power Supply
  - LM1117 3.3V fixed LDO
    - Readily Available
    - Used frequently
  Decision: LM1117 3.3V fixed LDO
  - Battery
    - CR123 – 1500mAh (Lithium)
    - CR2032 – 250mAh (Lithium)
  Decision: CR2032 X 2 (6.6V)

---
Design: Decisions Made
- LED
  - Time Division Multiplexing on LED's
    - 4017 Johnson counter with decoded outputs
    - MosFET drivers
    - Adjustable Pots on RGB Channels for different LED foreword voltages
  - Support RGB LEDs

---
Implementation:
Schematics

---
Implementation:
Microcontroller

---
Implementation:
Gyroscope

---
Implementation:
Power System

---
Implementation:
Decade Counter

---
Implementation:
Red, Blue, Green

---
Prototyping

---
Prototyping:
Spinning with Gyroscope

---
Implementation:
PCB

---
Implementation:
Tools Employed
- EAGLE CAD
- AVR Studio 6.0
- Gantt Project/Microsoft Project
- Libreoffice

---
Implementation:
Tools Employed
- Skype
- Git
- Redmine
- AVRISP MKII Programmer
- AVR JTAG ICE3 Programmer/Debugger

---
IP, Prior Work
- Component Datasheets
- No other IP or prior work used

---
Testing
- Power Test: Check for bridges between Power, Ground, and 3.3V
- LED Test: Light up a single LED
- Scheduler Test: Light up all LEDs a single color
- Color Test: Light one LED at a time, Red, Green, then Blue
- Gyro Test: Light LEDs based on Gyro State

---
Results

---
Results

---
Modifications to Board Layout

---
Board Demo Videos

---
Contributions
- Matthew: Interface Module
- Vernon: Programming
- Yusuf: Test Plan, Components
- Tyler: PCB Layout, LED module

---
Lessons Learned:
- Reflow: One board at a time
- Reflow: Main components and hand-solder capacitors, resistors, and MOSFETs
- Don't reflow on through-hole components
- Slow is Fast
- More thorough test plan

---
Circuit Improvements
- 9V battery – Board density
- Angled power and ISP headers
- More 0-ohm resistor jumpers
- LED headers – all four sides
- LEDs directly on PCB
- Separate large components from small
- Higher gate voltage

---
Questions?