## Slide 1: System Design and Modeling: Frisbee That Lights Up Based On Measured Angular Acceleration and Velocity
Matthew Branstetter
Vernon Jones
Yusuf Qedan
Tyler Tricker
ECE411 Practicum Project – Operation Awesome
Electrical Computer Engineering, Portland State University

## Slide 2: Light-up Frisbee Level 0 Block Diagram
Module | Light Up Frisbee
Inputs | Power 6V from 2 lithium batteries
Outputs | 10 RGB LED’s 40 pins common anode configuration
Functionality | Based on the measured angular velocity 10 RGB LEDs will light up different patterns and colors
Light-up Frisbee
10 RGB LEDs
Power 5-7V

## Slide 3: Light-up Frisbee Level 1 Block Diagram
Logic Power Supply
Power 5v-7V
3.3 V
Logic Module
Lighting Module
RGB LED Outputs
Row Strobe and Reset
3.3 V
Red Column Blue Column
Green Column

## Slide 4: Logic Power Supply: Level 0 Block Diagram
Module | Logic Power Supply
Inputs | Power 5-7V from 2 lithium batteries
Outputs | Power 3.3V
Functionality | Maintains a constant output voltage of 3.3V
Logic Power Supply
Power 3.3V
Power 5-7V

## Slide 5: Logic Power Supply: Level 1 Block Diagram
Power 3.3V
Power 5-7V
Voltage Regulator
Diode
Cap
Cap
Decoupling

## Slide 6: Logic Module: Level 0 Block Diagram
Module | Logic Circuit | 
Inputs | Power 3.3V | 
Outputs | Row Strobe – Signal to the lighting circuit to activate the next LED. | Red Column – PWM for red brightness
 | Row Reset - Signal to the lighting circuit to return to LED0. | Blue Column – PWM for blue brightness
 |  | Green Column – PWM for blue brightness
Functionality | Measures a rotational velocity and outputs lighting signals as a function of the rotational velocities value. | 
Logic Circuit
Power 3.3V
Row Strobe
Row Reset
Red Column Blue Column
Green Column

## Slide 7: Logic Module: Level 1 Block Diagram
Power 3.3V
Row Strobe
Row Reset
Red Column Blue Column
Green Column
Gyroscope
ATTINY261
ZOUT

## Slide 8: Lighting Module: Level 0 Block Diagram
Lighting Module
RGB Strobe
RGB LED Outputs
Row Strobe and Reset
3.3 V
Module | Logic Circuit | 
Inputs | Row Strobe – Signal to the lighting circuit to activate the next LED. | Red Column – PWM for red brightness
 | Row Reset - Signal to the lighting circuit to return to LED0. | Blue Column – PWM for blue brightness
 |  | Green Column – PWM for blue brightness
Output | 10 RGB LED Outputs | 
Functionality | Takes lighting signals from the Logic Module and pulses LEDs according to the signal | 
5-7 V

## Slide 9: Lighting Module: Level 1 Block Diagram
RGB Strobe
RGB LED Anode Outputs
Row Strobe and Reset
3.3 V
4017 Decade Decoder
Transistor Array
Transistor Array
5-7V
Current Limiter
Red Column Green Column
Blue Column